SECTION 12 12 30

ART HANGING AND DISPLAY SYSTEMS

HOSPITALITY MARKETING/MENU DISPLAY

Display hidden notes to specifier. (Don't know how? Click Here)

Copyright 2016 - AS Hanging Display Systems - All rights reserved

Copyright 2016 - 2016 ARCAT, Inc. - All rights reserved

** NOTE TO SPECIFIER ** AS Hanging Display Systems; art and display interior specialty fittings.
This section is based on the products of AS Hanging Display Systems, which is located at:
8396 State Route 9
West Chazy, NY 12992 
Toll Free Tel: 866-935-6949 
Email: request info (info@ashanging.com)
Web: www.ashanging.com  
 [ Click Here ] for additional information.
AS Hanging Display Systems has been active in the area of art and display and interior specialty fittings since 1964, and a manufacturer and distributor of hanging systems for more than two decades, having completed over 35,000 installations in North America.
The breadth of product lines, quality of solutions, and professional service enables the company to continue leadership in providing unique hardware support for art, display materials and signage to a vast variety of business categories and institutions including museums and art galleries, custom framing enterprises, retail stores, education, libraries, commercial office buildings, hospitality and health care markets.
After all, we honestly believe that when you call you are choosing to do business with us, the people that collectively make AS Hanging Display Systems. We believe you choose to do business with people and not a company. Hang with the Best®

- GENERAL

  - RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

    - Section 06 10 00 - Rough Carpentry.

  - SUBMITTALS

    - Submit under provisions of Section 01 30 00 - Administrative Requirements.

    - Product Data: Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - LEED Submittals:

      - Product Data for Credit MR 4.1 and Credit MR 4.2: For products having recycled content, submit documentation indicating percentages by weight of postconsumer and preconsumer recycled content. Include statement indicating cost for each product having recycled content.

      - Product Data for Credit EQ 4.2: For paints and coatings, submit documentation including VOC content.

      - Product Certificates for Credit MR 5.1 and Credit MR 5.2: For products and materials required to comply with requirements for regional materials, submit certificates indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include statement indicating distance to Project, cost for each regional material, and fraction by weight that is considered regional.

** NOTE TO SPECIFIER ** Include Shop Drawings only for work that involves custom fabrication or if Shop Drawings are typically prepared to assist in the performance of the work involved. Delete if not required.

    - Shop Drawings: Include details of construction, and relationship with adjacent construction.

    - Verification Samples: For each finish product specified, two samples, minimum size 6 inches square representing actual product, color, and patterns.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Minimum 5 year experience manufacturing similar products.

    - Installer Qualifications: Minimum 2 year experience installing similar products.

** NOTE TO SPECIFIER ** Include a mock-up if the project size and/or quality warrant taking such a precaution. The following is one example of how a mock-up on a large project might be specified. When deciding on the extent of the mock-up, consider all the major different types of work on the project.

    - Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

      - Finish areas designated by Architect.

      - Do not proceed with remaining work until workmanship is approved by Architect.

      - Remodel mock-up area as required to produce acceptable work.

  - PRE-INSTALLATION MEETINGS

    - Convene minimum two weeks prior to starting work of this section.

  - DELIVERY, STORAGE, AND HANDLING

    - Deliver and store products in manufacturer's unopened packaging bearing the brand name and manufacturer's identification until ready for installation.

    - Handling: Handle materials to avoid damage.

  - PROJECT CONDITIONS

    - Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's recommended limits.

  - SEQUENCING

    - Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

  - WARRANTY

    - Warranty: Submit manufacturer's standard limited one year warranty.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: AS Hanging Display Systems, which is located at: 8396 State Route 9; West Chazy, NY 12992 ; Toll Free Tel: 866-935-6949 ; Email: request info (info@ashanging.com); Web: www.ashanging.com

    - Web: http://www.ashanging.com.

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

    - Substitutions: Not permitted.

    - Requests for substitutions will be considered in accordance with provisions of Section 01 60 00 - Product Requirements.

** NOTE TO SPECIFIER ** Menu Display Kits from AS Hanging Display Systems are designed to easily display restaurant, cafe or corporate food service menus. These kits supply everything you need to present menus, daily specials, reviews, photos and upcoming events in your windows, reception alcove or waiting area. Insert pages or photos, up to 8.5 x 11 inch (portrait orientation, into clear acrylic pockets via top openings. Changes are made without tools. Delete if not required.

  - WORKPLACE SOLUTIONS

    - Menu Display Kit as manufactured by AS Hanging Display Systems.

      - Each Kit Includes:

        - Stainless Steel Cables: 10 feet, to be field trimmed.

        - Articulated Piers: To attach cables to walls, window returns, ceilings, or floors.

        - Mounting Hardware, including Decorative Mounting Plates to distribute forces against crushable surfaces.

        - Acrylic Pockets: Portrait orientation 8.5 x 11 inch live area.

        - Clamps: Single and/or double-sided side clamps.

        - Cable Trim Kit.

** NOTE TO SPECIFIER ** Delete kits not required.

      - Kit Identifier: K5011AA

        - Number of pockets: 1 (1 column x 1 row)

      - Kit Identifier: K5012AA

        - Number of pockets: 2 (1 column x 2 rows)

      - Kit Identifier: K5013AA

        - Number of pockets: 3 (1 column x 3 rows)

      - Kit Identifier: K5021AA

        - Number of pockets: 2 (2 columns x 1 row)

      - Kit Identifier: K5031AA

        - Number of pockets: 3 (3 columns x 1 row)

** NOTE TO SPECIFIER ** Custom configurations are available. Contact our customer service department to discuss options for custom configurations.

      - Custom Configuration:

        - Track Width: ______.

        - Number of Pockets: ______.

      - Custom Configuration: As detailed on Drawings.

      - Compatibility: Mount to window header/sill, window returns, walls, ceiling/floor in any combination.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

  - PREPARATION

    - Clean surfaces thoroughly prior to installation.

    - Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

  - INSTALLATION

** NOTE TO SPECIFIER ** Installation guidelines are provided with each shipment and are also downloadable at ASHanging.com.

    - Install in accordance with manufacturer's instructions, approved submittals, and in proper relationship with adjacent construction.

  - CLEANING

    - Clean installed system and remove excess materials.

    - Deliver any unused cable and fittings to Owner.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION