SECTION 12 12 30

ART HANGING AND DISPLAY SYSTEMS

PIER BASED CABLE SYSTEM

Display hidden notes to specifier. (Don't know how? Click Here)

Copyright 2016 - AS Hanging Display Systems - All rights reserved

Copyright 2016 - 2016 ARCAT, Inc. - All rights reserved

** NOTE TO SPECIFIER ** AS Hanging Display Systems; art and display interior specialty fittings.
This section is based on the products of AS Hanging Display Systems, which is located at:
8396 State Route 9
West Chazy, NY 12992 
Toll Free Tel: 866-935-6949 
Email: request info (info@ashanging.com)
Web: www.ashanging.com  
 [ Click Here ] for additional information.
AS Hanging Display Systems has been active in the area of art and display and interior specialty fittings since 1964, and a manufacturer and distributor of hanging systems for more than two decades, having completed over 35,000 installations in North America.
The breadth of product lines, quality of solutions, and professional service enables the company to continue leadership in providing unique hardware support for art, display materials and signage to a vast variety of business categories and institutions including museums and art galleries, custom framing enterprises, retail stores, education, libraries, commercial office buildings, hospitality and health care markets.
After all, we honestly believe that when you call you are choosing to do business with us, the people that collectively make AS Hanging Display Systems. We believe you choose to do business with people and not a company. Hang with the Best®

- GENERAL

  - RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

    - Section 06 10 00 - Rough Carpentry.

  - SUBMITTALS

    - Submit under provisions of Section 01 30 00 - Administrative Requirements.

    - Product Data: Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - LEED Submittals:

      - Product Data for Credit MR 4.1 and Credit MR 4.2: For products having recycled content, submit documentation indicating percentages by weight of postconsumer and preconsumer recycled content. Include statement indicating cost for each product having recycled content.

      - Product Data for Credit EQ 4.2: For paints and coatings, submit documentation including VOC content.

      - Product Certificates for Credit MR 5.1 and Credit MR 5.2: For products and materials required to comply with requirements for regional materials, submit certificates indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include statement indicating distance to Project, cost for each regional material, and fraction by weight that is considered regional.

** NOTE TO SPECIFIER ** Include Shop Drawings only for work that involves custom fabrication or if Shop Drawings are typically prepared to assist in the performance of the work involved. Delete if not required.

    - Shop Drawings: Include details of construction, and relationship with adjacent construction.

    - Verification Samples: For each finish product specified, two samples, minimum size 6 inches square representing actual product, color, and patterns.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Minimum 5 year experience manufacturing similar products.

    - Installer Qualifications: Minimum 2 year experience installing similar products.

** NOTE TO SPECIFIER ** Include a mock-up if the project size and/or quality warrant taking such a precaution. The following is one example of how a mock-up on a large project might be specified. When deciding on the extent of the mock-up, consider all the major different types of work on the project.

    - Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

      - Finish areas designated by Architect.

      - Do not proceed with remaining work until workmanship is approved by Architect.

      - Remodel mock-up area as required to produce acceptable work.

  - PRE-INSTALLATION MEETINGS

    - Convene minimum two weeks prior to starting work of this section.

  - DELIVERY, STORAGE, AND HANDLING

    - Deliver and store products in manufacturer's unopened packaging bearing the brand name and manufacturer's identification until ready for installation.

    - Handling: Handle materials to avoid damage.

  - PROJECT CONDITIONS

    - Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's recommended limits.

  - SEQUENCING

    - Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

  - WARRANTY

    - Warranty: Submit manufacturer's standard limited one year warranty.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: AS Hanging Display Systems, which is located at: 8396 State Route 9; West Chazy, NY 12992 ; Toll Free Tel: 866-935-6949 ; Email: request info (info@ashanging.com); Web: www.ashanging.com

    - Web: http://www.ashanging.com.

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

    - Substitutions: Not permitted.

    - Requests for substitutions will be considered in accordance with provisions of Section 01 60 00 - Product Requirements.

** NOTE TO SPECIFIER ** TENSIONED vs. SUSPENDED CABLES/RODS: Simply, suspended cable/rod systems suspend cable/rod from above. All of the following track-based systems will accomplish that.
For sleek, architectural impact, a Tensioned Cable System offers an engineered appearance that allows displayed items to "float" in front of a wall surface, tensioned between the ceiling and the floor (or between upper and lower points). Using specialized picture hanging hardware, the cable is attached from an upper track down to a lower track, or alternately, between pairs of standoffs (piers), allowing the cable to be tensioned between the upper and lower points. The result is a sophisticated, modern look that features parallel cables running from above to below the hanging object. The company's rod based systems may be deployed in similar manner. Tensioned Cable Hanging System hardware may be used to add tension to any of AS Hanging track-based cable systems except those based on the Display Reveal. 
Alternatively, you can use the company's standoff components, point-to-point piers, in place of tracks to create a clean, organized, and aesthetically pleasing display. The pier-based cable system is recommended if you are looking to create a permanently mounted display. Ideal uses include window merchandising, visual space dividers, directional signage, art, municipal announcements or even cafe menus, etc. If you plan to reposition your cables and rods frequently, a track-based solution is recommended as they allow changes to horizontal spacing with ease.

** NOTE TO SPECIFIER ** Pier Based Tensioned Cable System is a cable-based solution deployed from commercial strength standoffs/piers to be mounted to walls/ceilings/floors, or other similar surfaces. Use only stainless steel cables. Point-to-point piers used in place of tracks to create a clean, organized, and aesthetically pleasing display. The pier-based cable system is recommended if you are looking to create a permanently mounted display. Ideal uses include window merchandising, visual space dividers, directional signage, art, municipal announcements or even cafe menus, etc. If you plan to reposition cables and rods frequently, a track system is recommended. Consult AS Hanging for the best hanging configuration of cables, hooks and specialty fittings once building is occupied and art, display materials, notices and signage have been selected including framed and non-framed media due to weight and other variations among the objects to be hung. Delete if not required.

  - TENSIONED CABLE AND DISPLAY SYSTEM

    - Pier Based Cable System as manufactured by AS Hanging Display Systems. Provide materials and components required to provide a complete system by AS Hanging Display Systems for hanging corporate branding, display materials, informational and directional signage, art and regulatory notices, from point-to-point piers as indicated or scheduled. Refer to Drawings.

** NOTE TO SPECIFIER ** The system is configured from two or more cables, each held in tension between an upper and lower pier. Delete configuration not required.

      - Configuration: Fixed Piers, brushed nickel finish (mounted to horizontal surfaces).

      - Configuration: Articulated Piers, brushed nickel finish.

      - Aesthetic: Commercial grade piers/standoffs for art display and display making.

**NOTE TO SPECIFIER ** Decorative Mounting Plate is required when mounting piers to drywall, or other crushable, surface. Delete if not required.

      - Decorative Mounting Plate, brushed nickel finish

** NOTE TO SPECIFIER ** Delete cable length not needed. Cables are field trimmed to length.

      - Cable Length: 10 ft., Stainless Steel

      - Cable Length: 20 ft., Stainless Steel (Fixed Pier only)

    - Hooks: Provide manufacturer's recommended type and quantity of hooks needed to complete the intended display.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

  - PREPARATION

    - Clean surfaces thoroughly prior to installation.

    - Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

  - INSTALLATION

** NOTE TO SPECIFIER ** Installation guidelines are provided with each shipment and are also downloadable at ASHanging.com.

    - Install in accordance with manufacturer's instructions, approved submittals, and in proper relationship with adjacent construction.

  - CLEANING

    - Clean installed system and remove excess materials.

    - Deliver any unused cable and fittings to Owner.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION