SECTION 12 12 30

ART HANGING AND DISPLAY SYSTEMS

WORKPLACE SOLUTIONS

Display hidden notes to specifier. (Don't know how? Click Here)

Copyright 2016 - AS Hanging Display Systems - All rights reserved

Copyright 2016 - 2016 ARCAT, Inc. - All rights reserved

** NOTE TO SPECIFIER ** AS Hanging Display Systems; art and display interior specialty fittings.
This section is based on the products of AS Hanging Display Systems, which is located at:
8396 State Route 9
West Chazy, NY 12992 
Toll Free Tel: 866-935-6949 
Email: request info (info@ashanging.com)
Web: www.ashanging.com  
 [ Click Here ] for additional information.
AS Hanging Display Systems has been active in the area of art and display and interior specialty fittings since 1964, and a manufacturer and distributor of hanging systems for more than two decades, having completed over 35,000 installations in North America.
The breadth of product lines, quality of solutions, and professional service enables the company to continue leadership in providing unique hardware support for art, display materials and signage to a vast variety of business categories and institutions including museums and art galleries, custom framing enterprises, retail stores, education, libraries, commercial office buildings, hospitality and health care markets.
After all, we honestly believe that when you call you are choosing to do business with us, the people that collectively make AS Hanging Display Systems. We believe you choose to do business with people and not a company. Hang with the Best®

- GENERAL

  - RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

    - Section 06 10 00 - Rough Carpentry.

  - SUBMITTALS

    - Submit under provisions of Section 01 30 00 - Administrative Requirements.

    - Product Data: Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - LEED Submittals:

      - Product Data for Credit MR 4.1 and Credit MR 4.2: For products having recycled content, submit documentation indicating percentages by weight of postconsumer and preconsumer recycled content. Include statement indicating cost for each product having recycled content.

      - Product Data for Credit EQ 4.2: For paints and coatings, submit documentation including VOC content.

      - Product Certificates for Credit MR 5.1 and Credit MR 5.2: For products and materials required to comply with requirements for regional materials, submit certificates indicating location of material manufacturer and point of extraction, harvest, or recovery for each raw material. Include statement indicating distance to Project, cost for each regional material, and fraction by weight that is considered regional.

** NOTE TO SPECIFIER ** Include Shop Drawings only for work that involves custom fabrication or if Shop Drawings are typically prepared to assist in the performance of the work involved. Delete if not required.

    - Shop Drawings: Include details of construction, and relationship with adjacent construction.

    - Verification Samples: For each finish product specified, two samples, minimum size 6 inches square representing actual product, color, and patterns.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: Minimum 5 year experience manufacturing similar products.

    - Installer Qualifications: Minimum 2 year experience installing similar products.

** NOTE TO SPECIFIER ** Include a mock-up if the project size and/or quality warrant taking such a precaution. The following is one example of how a mock-up on a large project might be specified. When deciding on the extent of the mock-up, consider all the major different types of work on the project.

    - Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

      - Finish areas designated by Architect.

      - Do not proceed with remaining work until workmanship is approved by Architect.

      - Remodel mock-up area as required to produce acceptable work.

  - PRE-INSTALLATION MEETINGS

    - Convene minimum two weeks prior to starting work of this section.

  - DELIVERY, STORAGE, AND HANDLING

    - Deliver and store products in manufacturer's unopened packaging bearing the brand name and manufacturer's identification until ready for installation.

    - Handling: Handle materials to avoid damage.

  - PROJECT CONDITIONS

    - Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's recommended limits.

  - SEQUENCING

    - Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

  - WARRANTY

    - Warranty: Submit manufacturer's standard limited one year warranty.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: AS Hanging Display Systems, which is located at: 8396 State Route 9; West Chazy, NY 12992 ; Toll Free Tel: 866-935-6949 ; Email: request info (info@ashanging.com); Web: www.ashanging.com

    - Web: http://www.ashanging.com.

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

    - Substitutions: Not permitted.

    - Requests for substitutions will be considered in accordance with provisions of Section 01 60 00 - Product Requirements.

** NOTE TO SPECIFIER ** Our collection of pre-packaged business products include novel bulletin boards, easels that have no footprint, solutions for menu displays, and a method for displaying Get Well cards in patient stay rooms. Browse through AS Hanging's workplace solutions to find a display system that meets the demands of any workplace or business. Delete if not required.

  - WORKPLACE SOLUTIONS

    - Bulletin Bar/Horizontal Bulletin Bar: Casso Display Rail as manufactured by AS Hanging Display Systems. Features an internal wiper to grasp display papers. Display material inserts from below display rail.

      - Material: Extruded aluminum.

      - Bulletin bar/ display rail system that eliminates use of:

        - Tacks, push pins, staples, and other fasteners for displayed items.

        - Rollers to hold displayed items (eliminates binding even with stapled items).

        - Hinge type mechanisms.

      - Extendable on both ends in a continuous installation.

      - End Caps: Matching finish of extrusion.

      - Readily accepts variable material thicknesses up to 2mm thick (mat board mounted art).

      - Mounting:

        - Does not require direct fastening.

        - May be mounted to gypsum board, plaster and lath, brick, concrete block, and a variety of other wall surfaces,

        - May be mounted behind crown moldings, other finish carpentry, or other interior design features.

        - Shall not have exposed fasteners.

        - Shall not be drilled to receive fasteners.

        - Fasteners and hardware shall be supplied for mounting.

** NOTE TO SPECIFIER **Delete track length not required. Track may mounted end-to-end in a continuous run.

      - Track Length:

        - 24 inches.

        - 72 inches.

      - Finish:

** NOTE TO SPECIFIER **Delete finish not required.

        - Anodized, Silver Satin.

        - Powder Coat, White.

** NOTE TO SPECIFIER ** The Boardless® Bulletin Board from AS Hanging Display Systems is the answer to disorganized and cluttered ad hoc bulletin boards. Comprised of acrylic pockets that are organized in rows and columns, the structure lends, and forces, a more organized appearance. Simply insert and remove posts to the pockets as needed. It is an "always ready" design as no fasteners are required. These structured bulleting boards are particularly effective where the target audience is comprised of multiple special interest groups such as at libraries, community centers, health clubs, HOA club houses, sport centers, country clubs, etc. In these situations a pocket(s) can be allocated to a special interest and this group can always expect their material in the same location. Boardless boards are expandable by adding additional pockets and/or cables to the initial kit. Delete if not required.

    - Boardless Bulletin Board as manufactured by AS Hanging Display Systems. Each kit is to consist of upper and lower track (Silver Satin finish extruded aluminum Wall Track), all mounting hardware (consisting of painted head screws and screw anchors), stainless steel cables (10 ft. in length), acrylic pockets (portrait orientation 8.5 x 11 inch live area), single and/or double-sided side clamps. Cables are trimmed in the field and Cable Trim Kit is included. Delete kits not required.

      - Kit Identifier: K6031EC

        - Track Width: 3 feet

        - Number of Pockets: 3 (3 columns x 1 row)

      - Kit Identifier: K6032EC

        - Track Width: 3 feet

        - Number of Pockets: 6 (3 columns x 2 rows)

      - Kit Identifier: K6033EC

        - Track Width: 3 feet

        - Number of Pockets: 9 (3 columns x 3 rows)

      - Kit Identifier: K6034EC

        - Track Width: 3 feet

        - Number of Pockets: 12 (3 columns x 4 rows)

      - Kit Identifier: K6242EC

        - Track Width: 6 feet

        - Number of Pockets: 8 (4 columns x 2 rows)

      - Kit Identifier: K6243EC

        - Track Width: 6 feet

        - Number of Pockets: 12 (4 columns x 3 rows)

      - Kit Identifier: K6252EC

        - Track Width: 6 feet

        - Number of Pockets: 10 (5 columns x 2 rows)

      - Kit Identifier: K6253EC

        - Track Width: 6 feet

        - Number of Pockets: 15 (5 columns x 3 rows)

      - Kit Identifier: K6262EC

        - Track Width: 6 feet

        - Number of Pockets: 12 (6 columns x 2 rows)

      - Kit Identifier: K6263EC

        - Track Width: 6 feet

        - Number of Pockets: 18 (6 columns x 3 rows)

      - Kit Identifier: K6264EC

        - Track Width: 6 feet

        - Number of Pockets: 24 (6 columns x 4 rows)

      - Kit Identifier: K6281EC

        - Track Width: 6 feet

        - Number of Pockets: 8 (8 columns x 1 row)

      - Kit Identifier: K6282EC

        - Track Width: 6 feet

        - Number of Pockets: 16 (8 columns x 2 rows)

** NOTE TO SPECIFIER ** Custom configurations are available. Contact our customer service department to discuss options for custom configurations.

      - Custom Configuration:

        - Track Width: ______.

        - Number of Pockets: ______.

      - Custom Configuration: As detailed on Drawings.

** NOTE TO SPECIFIER ** The Footprintless® Easel from AS Hanging Display Systems overcomes the weaknesses of common office easels. Let's face it. As an architect and design professional you have to account for storage closets to store such things as easels for conference rooms. Then the common easel, with one leg longer that the other two, does not "store" well. When it comes to use these conference room easels often before top heavy and unstable during a presentation. The height is fixed and we all know how hard it is to write on an easel pad when writing below waist level. Footprintless Easel fixes all of this. It is mounted to the wall and is always ready without consuming precious space. No tripping or egress issues. It can hold an easel pad, any mount board and individual paper sheets. However, all of these are adjustable in height - presenters may adjust their materials to their height and comfort. For custom variations, contact our customer service group. Delete if not required.

    - Footprintless Easel as manufactured by AS Hanging Display Systems is the basis of design. Easels are wall mounted and have a span height of 48 inches. Each kit consists of upper and lower track (Wall Track), all mounting hardware (consisting of painted screw heads and screw anchors), preconfigured stainless steel cables with the required specialty hooks. Delete kits not required.

** NOTE TO SPECIFIER **Delete track color not required.

      - Track Color: Silver Satin.

      - Track Color: Black.

** NOTE TO SPECIFIER **Delete size not required.

      - Size: Single: 36 inches.

      - Size: Double: 72 inches. (Double-wide easel includes two pair of cable hardware sets.)

** NOTE TO SPECIFIER **Healthcare/Patient Care: Greeting Card Wall Organizer Casso® Display Rail from AS Hanging Display Systems solves a nuisance problem in patient care facilities. What to do with Get Well cards? Typically they are placed on the small horizontal surface that doubles as a table from which meds and food are distributed. The surface is simply too small. The cards frequently fall to the floor where them become the vector for transferring germs to the food/meds surface. Besides, it is a highly trained, precious and over worked resource that picks these up - a medical professional. A wall segment will host a length of display rail for the purpose of displaying and holding Get Well cards within view but out of the way. Simply insert and remove cards to read. No fasteners are needed. It features closed face track that hides all mounting hardware and blends nicely into a wide variety of interior design schemes and also makes it acceptable to Infectious Disease Control. In the Pediatrics Dept. the same rail can hold child patient art with the same ease.

    - Healthcare/Patient Care: Greeting Card Wall-Organizer. Casso Display Rail as manufactured by AS Hanging Display Systems. Features an internal wiper to grasp display papers. Display material inserts from below display rail.

      - Material: Extruded aluminum.

      - Bulletin bar/ display rail system that eliminates use of:

        - Tacks, push pins, staples, and other fasteners for displayed items.

        - Rollers to hold displayed items (eliminates binding even with stapled items).

        - Hinge type mechanisms.

      - Extendable on both ends in a continuous installation.

      - End Caps: Matching finish of extrusion.

      - Readily accepts variable material thicknesses up to 2mm thick (mat board mounted art).

      - Mounting:

        - Does not require direct fastening.

        - May be mounted to gypsum board, plaster and lath, brick, concrete block, and a variety of other wall surfaces,

        - May be mounted behind crown moldings, other finish carpentry, or other interior design features.

        - Shall not have exposed fasteners.

        - Shall not be drilled to receive fasteners.

        - Fasteners and hardware shall be supplied for mounting.

** NOTE TO SPECIFIER **Delete track length not required. Track may mounted end-to-end in a continuous run.

      - Track Length:

        - 24 inches.

        - 72 inches.

      - Finish:

** NOTE TO SPECIFIER **Delete finish not required.

        - Anodized, Silver Satin.

        - Powder Coat, White.

** NOTE TO SPECIFIER **Menu Display Kits from AS Hanging Display Systems are designed to easily display restaurant, cafe or corporate food service menus. These kits supply everything you need to present menus, daily specials, reviews, photos and upcoming events in your windows, reception alcove or waiting area. Insert pages or photos, up to 8.5 x 11 inch (portrait orientation, into clear acrylic pockets via top openings. Changes are made without tools. Delete if not required.

    - Menu Display Kit as manufactured by AS Hanging Display Systems.

      - Each Kit Includes:

        - Stainless Steel Cables: 10 feet, to be field trimmed.

        - Articulated Piers: To attach cables to walls, window returns, ceilings, or floors.

        - Mounting Hardware, including Decorative Mounting Plates to distribute forces against crushable surfaces.

        - Acrylic Pockets: Portrait orientation 8.5 x 11 inch live area.

        - Clamps: Single and/or double-sided side clamps.

        - Cable Trim Kit.

** NOTE TO SPECIFIER ** Delete kits not required.

      - Kit Identifier: K5011AA

        - Number of pockets: 1 (1 column x 1 row)

      - Kit Identifier: K5012AA

        - Number of pockets: 2 (1 column x 2 rows)

      - Kit Identifier: K5013AA

        - Number of pockets: 3 (1 column x 3 rows)

      - Kit Identifier: K5021AA

        - Number of pockets: 2 (2 columns x 1 row)

      - Kit Identifier: K5031AA

        - Number of pockets: 3 (3 columns x 1 row)

** NOTE TO SPECIFIER ** Custom configurations are available. Contact our customer service department to discuss options for custom configurations.

      - Custom Configuration:

        - Track Width: ______.

        - Number of Pockets: ______.

      - Custom Configuration: As detailed on Drawings.

      - Compatibility: Mount to window header/sill, window returns, walls, ceiling/floor in any combination.

- EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

  - PREPARATION

    - Clean surfaces thoroughly prior to installation.

    - Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

  - INSTALLATION

** NOTE TO SPECIFIER ** Installation guidelines are provided with each shipment and are also downloadable at ASHanging.com.

    - Install in accordance with manufacturer's instructions, approved submittals, and in proper relationship with adjacent construction.

  - CLEANING

    - Clean installed system and remove excess materials.

    - Deliver any unused cable and fittings to Owner.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION